## Slide 1
Hydrologic sensitivities
Julie Vano
Research while at:
University of Washington
Oregon State University
Key Collaborators: Dennis Lettenmaier (UCLA), Phil Mote (OSU),
Bart Nijssen (UW), Alan Hamlet (Notre Dame), David Rupp (OSU)
June 21, 2016
Meeting at U.S. Army Corps of Engineers, Seattle District Office
Notes: 1

## Slide 2: What are hydrologic sensitivities?

## Slide 3
Precipitation
Elasticity (ε)
Q ref+Δ% - Qref
Qref
Δ%
=
Temperature
Sensitivity (S)
Q ref+Δ - Qref
Qref
Δ°C
=
Notes: temperature (additive) and precipitation (percentage)

## Slide 4: How are hydrologic sensitivities useful?

## Slide 5: 1. Help explain how hydrology models differ

## Slide 6: Colorado River flows, mid 21st Century
Information from Table 5-1 in Western Water Assessment report to the Colorado Water Conservation Board “Colorado Climate Change: A Synthesis to Support Water Resource Management and Adaptation.” Oct 2008 (available online at: http://cwcb.state.co.us/NR/rdonlyres/8118BBDB-4E54-4189-A354-3885EEF778A8/0/CCSection5.pdf)
6

## Slide 7
Spatial Hydrologic Sensitivities for VIC
Temperature
Sensitivity (S)
Q ref+0.1°C - Qref
Qref
0.1 °C
=
Precipitation
Elasticity (ε)
Q ref+1% - Qref
Qref
1%
=
Lees
Ferry
Lees
Ferry
At Lees Ferry for the historical reference period:
ε= 2.2 and S = 6.5% per °C
Figure from Vano et al., JHM, 2012

## Slide 8
Spatial Hydrologic Sensitivities for Six Land Surface Models

## Slide 9
Studies using various approaches:
Seager et al. 2007; Seager et al. 2013
Milly et al. 2005
Christensen et al. 2004; Christensen and Lettenmaier, 2007; Cayan et al. 2010; USBR 2011
Gao et al. 2011; Rasmussen et al. 2011
Gao et al. 2012
Hoerling and Eischeid 2007
Cook et al. 2004
Woodhouse et al. 2006; McCabe and Wolock 2007; Meko et al. 2007; USBR 2011
Abbreviations:
GCM – Global Climate Model
RCM – Regional Climate Model
PDSI – Palmer Drought Severity Index
P – Precipitation
T – Temperature
R – Runoff
E – Evaporation
S. downscaling – statistical downscaling
GCMs, Emission scenarios,
Spatial resolution
Land surface representation
Approaches to generating future streamflow projections
Figure from Vano et al., BAMS, 2014

## Slide 10: 2. Provide quick calculations of long-term average changes, annually and seasonally

## Slide 11
Current approach:
Full-simulation approach
stream routing,
bias correcting
Global Climate
Model (PGCM,TGCM)
Future
streamflow
Hydrology
Models (e.g., VIC)
bias correcting,
downscaling
Global Climate
Model (ΔPGCM,ΔTGCM)
Quick approach:
Sensitivity-based approach
Hydrology
Sensitivities (ε,S)
count
% change in annual streamflow
Colorado R. at Lee’s Ferry in 2050s
count
% change in annual streamflow
Colorado R. at Lee’s Ferry in 2050s
Future streamflow
change (ΔQest)
?

## Slide 12
Full-simulation
approach
Future scenarios: Long-term annual average
Comparison of approaches for LONG-TERM annual change in
streamflow (Q)
dQsim = (Qsim-Qhist)/Qhist
Sensitivity-based
approach
dQest = ΔTGCM*Tsensivity+ ΔPGCM*Pelastcity + d(T,P)interaction (with 3 adjust.)

## Slide 13
B1 CDF
A2
A1B CDF
2010-2039
2040-2069
2070-2099
Sensitivity-based approach
Full-simulation approach
Cumulative distribution functions (CDFs) of 112 USBR simulations divided into time periods and emission scenarios.
A2 CDF

## Slide 14
Current approach:
Full-simulation approach
Yakima River naturalized flow (A1B)
stream routing,
bias correcting
Global Climate
Model (PGCM,TGCM)
Future
streamflow
Hydrology
Models (e.g., VIC)
bias correcting,
downscaling
Global Climate
Model (ΔPGCM,ΔTGCM)
Future streamflow
change (ΔQest)
?
Quick approach:
Sensitivity-based approach
Hydrology
Sensitivities (ε,S)

## Slide 15: Yakima River basin at Parker
Data from full-simulations were provided by Columbia Basin Climate Change Scenarios Project, UW, http://www.hydro.washington.edu/2860/.
Notes: I think units are cfs

## Slide 16: Yakima River basin at Parker
Data from full-simulations were provided by Columbia Basin Climate Change Scenarios Project, UW, http://www.hydro.washington.edu/2860/.

## Slide 17: Precipitation Temperature New Climate Change Projections
Figures from John Abataoglou at the University of Idaho
How does this translate into changes in streamflow?

## Slide 18: Precipitation Temperature New Climate Change Projections
Figures from John Abataoglou at the University of Idaho
How does this translate into changes in streamflow?
2007 GCMs

## Slide 19: Precipitation Temperature New Climate Change Projections
Figures from John Abataoglou at the University of Idaho
How does this translate into changes in streamflow?
2007 GCMs
2012 GCMs

## Slide 20
Yakima River Basin, streamflow estimates in 2050s
n is the number of GCMs for each emission scenario, preliminary results.
2007 GCMs
2012 GCMs
N=15
n=15
n=13
n=27
n=27

## Slide 21: 3. Help in selecting global climate models for a particular impact

## Slide 22
Lots of models, increasingly more information, impacts only considered at the end
Image from http://www.activatedesign.co.nz/blog/the-frustration-of-almost-perfect-websites/

## Slide 23
Are there ways to understand climate change impacts that are less computationally involved and focus on the impact you care most about?

## Slide 24: Good news, there is…
Not all models are created equal; we can be more selective in what we use

## Slide 25
Global Climate Model ranking for
Pacific Northwest by Rupp et al. JGR 2013

## Slide 26: Good news, there is…
Not all models are created equal; we can be more selective in what we use
Sensitivities of a particular impact (e.g., streamflow change) can provide plausible first-order estimates and aid model selection

## Slide 27
Global Climate Models precipitation and temperature responses
GCM ranking from Rupp et al. (JGR 2013), blue = RCP 4.5, red = RCP 8.5, Eastern Washington region 1970-1999 to 2041-2070
Notes: Use sensitivity as simple linear model
dF=a dT + b dP also dF=const. -a/b
(slope is elast / sensitivity)

## Slide 28
Global Climate Models precipitation and temperature responses
GCM ranking from Rupp et al. (JGR 2013), blue = RCP 4.5, red = RCP 8.5, Eastern Washington region 1970-1999 to 2041-2070
warmer,
wetter
less warm,
drier
less warm,
wetter
warmer,
drier
Notes: Use sensitivity as simple linear model
dF=a dT + b dP also dF=const. -a/b
(slope is elast / sensitivity)

## Slide 29
Willamette
Summer flows for fish
(June-August)
Yakima
Irrigation season
(April-September)
Upper Columbia
Spring snowmelt
(April-June)
Impact:
Seasonal Streamflow

## Slide 30
Temperature
Sensitivity (S)
Q ref+Δ°C - Qref
Qref
Δ°C
=
Yakima
Irrigation season
(April-September)
Vano, Kim, Rupp, and Mote, GRL, 2015.
Notes: Temperature: Summer in Willamette and Apr-Sep in Yakima, as temperatures increase, the decline per deg C becomes less (can only decrease streamflow by so much)
Spring in the Upper Columbia, temperatures result in flow increases (for smaller T changes), but once T changes are large the shift in the hydrograph is so big that flows in AMJ decline
Precipitation: In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5%.
In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5% (and it gets worse if I calc it for a 6 deg C change, 43.2% vs. -15.0%, where the sign actually changes).
Summer in Willamette and Apr-Sep in Yakima, as temperatures increase, the decline per deg C becomes less (can only decrease streamflow by so much)
Spring in the Upper Columbia, temperatures result in flow increases (for smaller T changes), but once T changes are large the shift in the hydrograph is so big that flows in AMJ decline

## Slide 31
Temperature
Sensitivity (S)
Q ref+Δ°C - Qref
Qref
Δ°C
=
Yakima
Irrigation season
(April-September)
Vano, Kim, Rupp, and Mote, GRL, 2015.
Notes: Temperature: Summer in Willamette and Apr-Sep in Yakima, as temperatures increase, the decline per deg C becomes less (can only decrease streamflow by so much)
Spring in the Upper Columbia, temperatures result in flow increases (for smaller T changes), but once T changes are large the shift in the hydrograph is so big that flows in AMJ decline
Precipitation: In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5%.
In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5% (and it gets worse if I calc it for a 6 deg C change, 43.2% vs. -15.0%, where the sign actually changes).

## Slide 32
Temperature
Sensitivity (S)
Q ref+Δ°C - Qref
Qref
Δ°C
=
Yakima
Irrigation season
(April-September)
Willamette
Summer flows for fish
(June-August)
Vano, Kim, Rupp, and Mote, GRL, 2015.
Notes: Temperature: Summer in Willamette and Apr-Sep in Yakima, as temperatures increase, the decline per deg C becomes less (can only decrease streamflow by so much)
Spring in the Upper Columbia, temperatures result in flow increases (for smaller T changes), but once T changes are large the shift in the hydrograph is so big that flows in AMJ decline
Precipitation: In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5%.
In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5% (and it gets worse if I calc it for a 6 deg C change, 43.2% vs. -15.0%, where the sign actually changes).

## Slide 33
Yakima
Irrigation season
(April-September)
Upper Columbia
Spring snowmelt
(April-June)
Temperature
Sensitivity (S)
Q ref+Δ°C - Qref
Qref
Δ°C
=
Willamette
Summer flows for fish
(June-August)
Vano, Kim, Rupp, and Mote, GRL, 2015.
Notes: Temperature: Summer in Willamette and Apr-Sep in Yakima, as temperatures increase, the decline per deg C becomes less (can only decrease streamflow by so much)
Spring in the Upper Columbia, temperatures result in flow increases (for smaller T changes), but once T changes are large the shift in the hydrograph is so big that flows in AMJ decline
Precipitation: In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5%.
In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5% (and it gets worse if I calc it for a 6 deg C change, 43.2% vs. -15.0%, where the sign actually changes).

## Slide 34
Varying temperature response
Vano, Kim, Rupp, and Mote, GRL, 2015.
Notes: Temperature: Summer in Willamette and Apr-Sep in Yakima, as temperatures increase, the decline per deg C becomes less (can only decrease streamflow by so much)
Spring in the Upper Columbia, temperatures result in flow increases (for smaller T changes), but once T changes are large the shift in the hydrograph is so big that flows in AMJ decline
Precipitation: In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5%.
In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5% (and it gets worse if I calc it for a 6 deg C change, 43.2% vs. -15.0%, where the sign actually changes).

## Slide 35
and constant precipitation response
Varying temperature response
Vano, Kim, Rupp, and Mote, GRL, 2015.
Notes: Temperature: Summer in Willamette and Apr-Sep in Yakima, as temperatures increase, the decline per deg C becomes less (can only decrease streamflow by so much)
Spring in the Upper Columbia, temperatures result in flow increases (for smaller T changes), but once T changes are large the shift in the hydrograph is so big that flows in AMJ decline
Precipitation: In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5%.
In the Upper Columbia, if we used the 1% perturbation instead of 20% and the change in P was 20%, we'd estimate a streamflow change of 21.6% instead of 20.2%. Alternatively, for T, if we used a 0.1 deg C instead of a 3 deg C and the change in temp was 3 deg C, we'd estimate a 21.6% change instead of a 5.5% (and it gets worse if I calc it for a 6 deg C change, 43.2% vs. -15.0%, where the sign actually changes).

## Slide 36
Global Climate Models precipitation and temperature changes
GCM ranking from Rupp et al. (JGR 2013), blue = RCP 4.5, red = RCP 8.5, lighter numbers indicate multiple runs for the same GCM, Eastern Washington region 1970-1999 to 2041-2070
Notes: Use sensitivity as simple linear model
dF=a dT + b dP also dF=const. -a/b
(slope is elast / sensitivity)

## Slide 37
Global Climate Models precipitation and temperature changes
and selection based on impact-relevant sensitivities
GCM ranking from Rupp et al. (JGR 2013), blue = RCP 4.5, red = RCP 8.5, lighter numbers indicate multiple runs for the same GCM, Eastern Washington region 1970-1999 to 2041-2070, contours of streamflow change derived from S and ε values
Yakima River basin
irrigation season
(Apr-Sep)
Notes: Use sensitivity as simple linear model
dF=a dT + b dP also dF=const. -a/b
(slope is elast / sensitivity)

## Slide 38
Global Climate Models precipitation and temperature changes
and selection based on impact-relevant sensitivities
GCM ranking from Rupp et al. (JGR 2013), blue = RCP 4.5, red = RCP 8.5, lighter numbers indicate multiple runs for the same GCM, Eastern Washington region 1970-1999 to 2041-2070, contours of streamflow change derived from S and ε values
Yakima River basin
irrigation season
(Apr-Sep)
Notes: Use sensitivity as simple linear model
dF=a dT + b dP also dF=const. -a/b
(slope is elast / sensitivity)

## Slide 39
Selecting climate scenarios in three river basins and seasons
Contours based on Variable Infiltration Capacity hydrologic model derived sensitivities, fig. from Vano et al., GRL, 2015
Notes: good performers, meaning they adequately simulate historical climate, providing plausible results for the region of interest

## Slide 40: 4. Help explain how future projections differ for the impact of interest
Note: as long as impacts are long-term seasonal (also shown earlier) or annual averages

## Slide 41
Willamette
Summer flows for fish
(June-August)
Yakima
Irrigation season
(April-September)
Upper Columbia
Spring snowmelt
(April-June)
Impact distributions for specific seasons
Streamflow
change
= S(ΔT) ΔT + ε ΔP
% streamflow change
% streamflow change
% streamflow change
Vano, Kim, Rupp, and Mote, GRL, 2015.

## Slide 42
RCP 26
RCP 45
2010-2039
2040-2069
2070-2099
RCP 60
RCP 85
Preliminary Results at Lees Ferry, Sensitivity-based approach estimation for AR5 GCMs
change in streamflow (%), difference relative to 1970-1999
One run per GCM
N=32
N=17
N=35
N=24

## Slide 43
RCP 26
RCP 45
2010-2039
2040-2069
2070-2099
RCP 60
RCP 85
Preliminary Results, Sensitivity-based approach estimation for AR5 GCMs
change in streamflow (%), difference relative to 1970-1999
All runs per GCM
N=65
N=33
N=67
N=50

## Slide 44: What are hydrologic sensitivities limitations?

## Slide 45: Considerations
Linearity, the extent to which a small change (e.g., 0.1 °C), which provides a reasonable approximation of the tangent of the change, is proportional to a larger change (e.g., 3 °C) which captures the secant
?
(2) Superposition, the extent to which hydrologic sensitivities identified through independent simulations can be added together to equal the same value as changes applied within the same simulation.
ΔQ1%P+ΔQ1°C= ΔQ1°C & 1%P
ΔQ3°C warm season+ ΔQ3°C cool season = ΔQ3°C year round
?

## Slide 46
(3) Considerations: Physical context
Temp. Sensitivity, S
(% runoff change per °C)
Precipitation
Elasticity, ε
ε:
S:

## Slide 47
Figure from Steve Burges, CEE 576, Physical Hydrology, Fall 2007
total storage relative to annual inflow ratios
4
0.3
(4) Considerations: Management context
Annual vs. seasonal responses

## Slide 48
Hydrologic sensitivities are a measure of long-term average changes. They cannot be used to evaluate extremes or used in reservoir operations modeling (or any evaluation that relies on a temporal sequence).

## Slide 49
How are hydrologic sensitivities useful:
Help explain how hydrology models differ
Provide quick calculations of long-term average changes, annually and seasonally
Help in selecting global climate model futures for a particular impact
Help explain how future projections differ
What are hydrologic sensitivities limitations:
Ability to use hydrologic sensitivities depends on linearity, superposition, physical and management context (not one size fits all)
Not for evaluating extremes or any evaluation that relies on temporal sequences
Overall:
Quick and complementary, can help set bounds and understand new scenarios
Emphasizes understanding of the system and impact, not just data processing
Summary
Notes: quantify local change through using concepts of hydrologic sensitivities to changes in central tendencies and extreme events.
Are there other approaches to understand climate change impacts that start with the impact?
(ideally ones that are less computationally involved)

## Slide 50: Acknowledgements
Feedback, questions??
Thanks to my co-authors, especially Dennis Lettenmaier, Bart Nijssen, Phil Mote, and Alan Hamlet.
Support for this work was provided by the National Science Foundation under Awards No. EAR-1250087 and EAR-1039192, by the U.S. National Oceanic and Atmospheric Administration, Grant NA10OAR4310218, and by USGS, Grant #G12AC20495
Vano, J. A., J. B. Kim, D. E. Rupp, and P. W. Mote (2015), Selecting climate change scenarios using impact-relevant sensitivities, Geophys. Res. Lett., 42, 5516–5525, doi:10.1002/2015GL063208.
Vano, JA, B Nijssen, and DP Lettenmaier, 2015: Seasonal hydrologic responses to climate change in the Pacific Northwest, Water Resources Research, 51(4), 1959-1976, doi:10.1002/2014WR015909

## Slide 51: More on seasonal sensitivities

## Slide 52
Projected precipitation changes over Pacific Northwest
Figure from Mote and Salathé (2009), Washington Climate Change Impacts Assessment.
Precipitation
Temperature
Notes: describe what’s shown in more detail (for example, the SRES scenarios, y and x axis, what is the box plot range).
Fig. 9 Range (lowest to highest) of projected changes in temperature for each season (DJF=winter, etc.), relative to the 1970-99 mean. In each pair of box- and-whiskers, the left one is for SRES scenario B1 and the right is A1B; circles are individual model values. Box-and-whiskers plots indicate 10th and 90th percentiles (whiskers), 25th and 75th percentiles (box ends), and median (solid middle bar) for each season and scenario. Not all values are visible due to symbol overlap. Printed values are the weighted Reliability Ensemble Average of all GCMs for the season and scenario.
Fig. 10 As in Figure 9, but for precipitation. The height of the bars indicates actual water precipitation but the percentages are calculated with respect to a reference value for that season, so that -11% in JJA is much less than -11% in DJF. The reference values for the extremes are that model’s 20th century mean for that season (or annual mean), and for the REA average the reference is the all-model 20th century value. Unlike for temperature, for any season some models project increases and some project decreases, though the vast majority project decreases for summer and increases for winter by the 2080s
Over PNW. defined as the region between 124° and 111° west longitude, 41.5° to 49.5° north latitude: Washington, Oregon, Idaho,
western Montana, and a small slice of adjacent states and British Columbia.
Models have different spatial resolutions, but the number of model grid
points enclosed in this latitude-longitude box is between 6 and 91.

## Slide 53
Seasonal responses to temperature change
S values:

## Slide 54
S values:
Seasonal responses to temperature change

## Slide 55
S values:
Seasonal responses to temperature change

## Slide 56
S values:
Seasonal responses to temperature change

## Slide 57
S values:
Seasonal responses to temperature change

## Slide 58: Seasonal Responses Yakima River basin at Parker
ε values:
S values:
96 values (ε and S) serve as transfer function

## Slide 59: Seasonal Responses Yakima River basin at Parker
ε values:
S values:
96 values (ε and S) serve as transfer function

## Slide 60: Application
Sequencing allows for the superposition of 0.1°C, while also capturing the interactions from larger increments of change
ε values:
S values:
Q1+Q1*ΔPOND*εOND = Q2
Q2+Q2*ΔTJFM*SJFM = Q3
and so on…
Q3+Q3*ΔPJFM*εJFM = Q4
Q4+Q4*ΔTAMJ*SAMJ = Q5
Q5+Q5*ΔPAMJ*εAMJ = Q6
Q6+Q6*ΔTJAS*SJAS = Q7
Q7+Q7*ΔPJAS*εJAS = Qfuture_flow
Qhis+Qhis*ΔTOND*SOND = Q1
Notes: Want to be able to capture the larger increment of change, but also have them distinct as the temperatures applied would be uniform. Important to capture the interatctions. How change from one season is effecting the other.
Reintroduce some of the effect of the large seasonal shifts without double counting snow melt… ant superposition of 0.1 deg C, but change increment is often greater, in which case it’s important to

## Slide 62
Data from full-simulations were provided by Columbia Basin Climate Change Scenarios Project, UW, http://www.hydro.washington.edu/2860/.
2040s for
A1B emissions

## Slide 63: Precipitation Temperature New Climate Change Projections
Figures from John Abataoglou at the University of Idaho
How does this translate into changes in streamflow?
2007 GCMs
2012 GCMs

## Slide 64
Percent diff is the change in annual magnitude, n is the number of GCMs for each emission scenario.
Yakima River Basin, streamflow estimates in 2080s

## Slide 65
Percent diff is the change in annual magnitude, n is the number of GCMs for each emission scenario.
ONLY
TEMP
Yakima River Basin, streamflow estimates in 2080s

## Slide 66
Differences in warm and cool season responses.
dark orange = largest change in seasonality
Sub-basin responses to changes in seasonal differences
S values:
cool season
warm season

## Slide 67
Sub-basin responses to changes in seasonal differences
2080 B1
Differences in warm and cool season responses.
dark orange = largest change in seasonality

## Slide 68: More on annual sensitivities

## Slide 69: Methodology
Catchment LSM
Community Land
Model 3.5 (CLM)
Noah 2.7 LSM
Noah 2.8 LSM
Sacramento (Sac)
Variable Infiltration
Capacity 4.0.6 (VIC)
Precipitation
Elasticity (ε)
Q ref+1% - Qref
Qref
1%
=
Land-surface Hydrologic Models
Measures
Temperature
Sensitivity (S)
Q ref+0.1 - Qref
Qref
0.1°C
=
Precipitation & Temperature Interactions
Notes: temperature (additive) and precipitation (percentage)

## Slide 70
Precipitation
Elasticity (ε)
Q ref+1% - Qref
Qref
1%
=
reference precipitation (100% = historical)
historic flows at Lees Ferry
P elast
Hydrologic Sensitivities at Lees Ferry
Figure from Vano et al., JHM, 2012

## Slide 71
Precipitation
Elasticity (ε)
Q ref+1% - Qref
Qref
1%
=
observed
(non-parametric estimator)
Hydrologic Sensitivities at Lees Ferry
average runoff (cms)
0 200 400 600 800 1000 1200 1400
historic flows at Lees Ferry
P elast
Temperature
Sensitivity (S)
Q ref+0.1°C - Qref
Qref
0.1 °C
=
reference temp in °C
(historical = 0)
T sens (%)
Figure from Vano et al., JHM, 2012

## Slide 72
Figure includes Temperature (dT) and Precipitation (dP) changes for GCMs used in Chistensen and Lettenmaier (2007).
GCM Temperature and Precipitation Changes
dPGCM (%)
dTGCM (°C)

## Slide 73: Adjustments
Ch 3, slide 73
Pre adjustments
Three adjustments that improve the correlation and minimized the range of our confidence interval:
Vary ε and S values as a function of dP and dT respectively
Incorporate monthly dT and S values instead of using the annual average
(3) Adjust monthly dP values to be consistent with downscaling adjustments
Note: interaction term is zero in the Colorado basin, based on Vano et al. (JHM, 2012)
Post adjustments

## Slide 74: Application to 112 simulations of USBR
GCMs: 16
Emission scenarios: A2, A1B, B1
Total projections: 112 (multiple runs)
Time period: 2020s, 2040s, 2080s
Spatial resolution: 1/8° (~12 km)
Land surface: Hydrologic model (VIC)
Ch 3, slide 74
Regressions appear to contain some heteroscedasticity.

## Slide 75: Extra slides

## Slide 76
Traditional
approach
stream routing,
bias correcting
Global Climate
Models (PGCM,TGCM)
Hydrology
Models (e.g., VIC)
bias correcting,
downscaling
Management
Models
Climate Impact (e.g.,
earlier runoff, floods)
Changes in
Central Tendencies
Climate Impact
(e.g., earlier runoff)
Global Climate
Models (ΔPGCM,ΔTGCM)
Sensitivity-based
approach
Hydrology
Sensitivities (ε,S)

## Slide 77
Traditional
approach
stream routing,
bias correcting
Global Climate
Models (PGCM,TGCM)
Hydrology
Models (e.g., VIC)
bias correcting,
downscaling
Management
Models
Climate Impact (e.g.,
earlier runoff, floods)
Changes in
Central Tendencies
Climate Impact
(e.g., earlier runoff)
Global Climate
Models
pattern matching,
over threshold
identify times
Definition Extreme
Event by Mgmt
Impact-driven
approach
Climate Impact
(e.g., floods)
iterate to define threshold for extreme event
Hydrology
Models (e.g., VIC)
Sensitivity-based
approach
Global Climate
Models (ΔPGCM,ΔTGCM)
Hydrology
Sensitivities (ε,S)

## Slide 78: Preliminary results: total runoff on December 29, 1917
count
1 day of weather
total runoff (mm)
Variable Infiltration Capacity (VIC) model, total runoff = base flow + runoff
single grid, elevation 1250 m
1 day of meteorological forcings (Dec 29, 1917)
initial historical conditions from Dec 28 (1916-2006)
red line = event magnitude
Notes: Historical conditions = state files (saved state of the model)

## Slide 79: Preliminary results: total runoff on December 29, 1917
total runoff (mm)
4 days of weather
(start Dec 26)
total runoff (mm)
1 day of weather
(start Dec 29)
total runoff (mm)
2 days of weather
(start Dec 28)
total runoff (mm)
3 days of weather
(start Dec 27)
Notes: Produced by initial states
With previous day’s conditions

## Slide 80: Preliminary results: total runoff on December 29, 1917
28 days 27 days 26 days 25 days 24 days 23 days 22 days
21 days 20 days 19 days 18 days 17 days 16 days 15 days
14 days 13 days 12 days 11 days 10 days 9 days 8 days
7 days 6 days 5 days 4 days 3 days 2 days 1 day
count

## Slide 81: Preliminary results: total runoff on December 29, 1917
total runoff (mm)
event magnitude
initial conditions in 1917
initial conditions (1916-2006)
days of weather
Notes: Regardless of what the initial conditions are if you have the sequence of events from Dec 12 to Dec 29 in 1917 (17 days) you will get a event of 135 mm.
If you have the sequence
Where this trace is from 19xx,

## Slide 82: Preliminary results: total runoff on December 29, 1917
event magnitude
initial conditions in 1917
initial conditions (1916-2006)
total runoff (mm)
1985
days of weather

## Slide 83: Preliminary results: total runoff on December 29, 1917
event magnitude
initial conditions in 1917
initial conditions (1916-2006)
total runoff (mm)
2005
days of weather

## Slide 84: Preliminary results: total runoff on December 29, 1917
total runoff (mm)
event magnitude
initial conditions in 1917
initial conditions (1916-2006)
days of weather
4 days
17 days
Notes: Regardless of what the initial conditions are if you have the sequence of events from Dec 12 to Dec 29 in 1917 (17 days) you will get a event of 135 mm.
If you have the sequence
Where this trace is from 19xx,

## Slide 85: Preliminary results: total runoff on November 12, 1999
days of weather
total runoff (mm)
event magnitude
initial conditions in 1999
initial conditions (1916-2006)

## Slide 86: Preliminary results: total runoff on November 12, 1999
days of weather
total runoff (mm)
event magnitude
initial conditions in 1999
initial conditions (1916-2006)

## Slide 87
What is the value of this information??

## Slide 88
How many days of weather are needed for X% likelihood to be greater than X?
Quantify flood characteristics
Event magnitude
Initial conditions in 1999
Initial conditions (1916-2006)
3 days of weather
Nov 12, 1999
P = 186 mm
T = 6.2 C
Nov 11, 1999
P = 32 mm
T = 5 C
Nov 10, 1999
P = 67 mm
T = 4.3 C
days of weather
November 12, 1999
Notes: For the sake of this example, here are the three largest floods. I increase the initial conditions
X are the thresholds
Increased to 90 years of record
Set threshold
Something about the output in these X days that is unique.
How long until X point is reached.

## Slide 89
Quantify flood characteristics
Event magnitude
Initial conditions in 1999
Initial conditions (1916-2006)
3 days of weather
Nov 12, 1999
P = 186 mm
T = 6.2 C
Nov 11, 1999
P = 32 mm
T = 5 C
Nov 10, 1999
P = 67 mm
T = 4.3 C
days of weather
150 mm
How many days of weather are needed for X% likelihood to be greater than 150 mm?
November 12, 1999
Notes: For the sake of this example, here are the three largest floods. I increase the initial conditions
X are the thresholds
Increased to 90 years of record
Set threshold
Something about the output in these X days that is unique.
How long until X point is reached.

## Slide 90
Quantify flood characteristics
Runoff greater than 150 mm
1 day: 28% of years
2 days: 39% of years
3 days: 81% of years
Event magnitude
Initial conditions in 1999
Initial conditions (1916-2006)
3 days of weather
Nov 12, 1999
P = 186 mm
T = 6.2 C
Nov 11, 1999
P = 32 mm
T = 5 C
Nov 10, 1999
P = 67 mm
T = 4.3 C
days of weather
150 mm
answer: 3 days
November 12, 1999
How many days of weather are needed for 50% likelihood to be greater than 150 mm?
Notes: For the sake of this example, here are the three largest floods. I increase the initial conditions
X are the thresholds
Increased to 90 years of record
Set threshold
Something about the output in these X days that is unique.
How long until X point is reached.

## Slide 91
Use several events (e.g., top 3 events) to characterize weather patterns that generate flooding.
Identify what ifs: the largest runoff event (1990) was at the high end of the ensemble of initial conditions, whereas the 3rd largest runoff event (2006) could have been larger
Quantify flood characteristics
Over 150 mm
1 day: 28%
2 days: 39%
3 days: 81%
Over 150 mm
1 day: 27%
2 days: 92%
3 days: 93%
Over 150 mm
1 day: 25%
2 days: 92%
3 days: 95%
Nov. 11, 1990 (biggest)
Nov. 12, 1999
Nov. 7, 2006
days of weather

## Slide 92: Reference past years
For example:
If snow and soil conditions were similar to 1995, the event would have been 15% greater.
Future projections show a __% increase in floods similar to those in November 1999 by the 2050s.
November 12, 1999
1995
Notes: Highlight range of top ten events
Why I think you might be interestedManagers amazing ability to recall past years

## Slide 93: Summary
The new bottom-up approach:
encourages decision-maker engagement at the beginning and throughout
looks at system vulnerabilities before looking at climate change
quantifies the familiar, how managers talk about extreme events
Next steps:
get feedback
quantify weather patterns and their frequency in global climate models
compare with conventional approach, are extremes different?
Notes: New bottom-up approach use the same models, but start with identifying the impact
encourages decision maker participation at - Can use this to identify how results in the future differ from those in the past.
Future directions: relevant flows in the Sauk, help in deciding which runs look at monthly streamflows for the Sauk